## Slide 1
GlucoSentinel: system architecture of the type 2 diabetes digital twin
Two data streams in, one calibrated virtual patient in the middle, a 2-hour spike warning and a doctor console out
1 Data sources
Static stream: EHR
Synthetic EHR
120 Synthea-style patients
HL7 FHIR R4 bundle
Condition, ICD-10 E11.9
Labs, LOINC (HbA1c 4548-4)
Medications, RxNorm
TCF7L2 genotype + PRS
Dynamic: wearables
CGM glucose
every 5 min
Smartwatch
heart rate, HRV RMSSD
Sleep stages
light, deep, REM, awake
Steps
per 5 min, walks
Meal log app
32 Indian dishes
2 Ingest
FHIR parser
bundle to EHR features
5-min grid
align all streams
Sensor QC
gaps, dropouts
Sleep debt score
per night
Meal events
carbs split by GI
3 Digital twin engine
A. EHR prior HbA1c, FPG, BMI, duration, genotype, meds set starting physiology
B. Calibrate 7-day onboarding: fit insulin sensitivity, beta-cell, basal, dawn
C. Assimilate nudge the twin to each CGM reading every 5 min
D. Simulate 2-hour forecast and what-if: meal swap, walk, sleep, meds
Physiology core (per patient)
Glucose dG/dt = -(SG + X)G + SG Gb(t) + Ra(t)/V - ex steps G
Insulin action dX/dt = -p2 X + p2 SI s(t) (I - Ib)
Insulin dI/dt = -n (I - Ib) + gamma max(G - Gb, 0)
Gut fast and slow carb pools by meal GI
Modifiers dawn effect, stress, sleep debt lowers SI s(t)
Learned per patient SI, gamma, Gb, dawn. Recovery of true insulin sensitivity: r = 0.92
4 Fusion and AI
81 fused features every 5 min
E 23
EHR
W 40
Wearables + CGM
R 5
Personal routine
T 13
Twin state
LightGBM classifier: P(spike above 180 in next 2 h)
4 LightGBM forecasters: +30, +60, +90, +120 min
SHAP: top drivers per alert
Alert policy: threshold set on validation, at most 1 per hour
5 Doctor and patient
Patient nudge
Spike likely after lunch
Try bajra roti instead of rice
Walk 20 min after eating
Doctor console
Risk card and alert
CGM plus 2-h forecast
Why panel (SHAP)
What-if simulator
Weekly AGP, TIR
FHIR record view
95 min
median warning lead
85%
spikes warned 30+ min ahead
0.82
false alerts per day
Governance, evaluation and stack
Data: synthetic only, no real patient data (DPDP Act, HIPAA sandbox)
Split: 84 / 12 / 24 patients, week 1 calibrates, week 2 evaluates
Checks: ablation, episode lead time, Clarke grid, subgroup AUROC
Stack: Python 3, NumPy, pandas, LightGBM, Streamlit, Plotly
Standards: HL7 FHIR R4, LOINC, ICD-10, RxNorm, ABDM ready
Licence: MIT open source; research prototype, not a medical device